## Slide 1: Passing Mobile Subscription Info over DHCP and RA
Saravanan Muthusamy
Yiu Lee
Ruchi Kothari
IETF118

## Slide 2: Problem Statement
It is common for mobile device (UA) to switch between WiFi and MN
In an environment where the WiFi network and MN network are the same provider, and the WiFi network uses simple PSK authentication rather than EAP-SIM or WPA-Enterprise, the network operator will want to get the active mobile subscription associated to the UA to provide service continuity and/or enhanced experience.

## Slide 3: Mobile-Sub-Info Option
Define a new option “Mobile-Sub-Info” in DHCP, DHCPv6 and RA.
The option contains a network URI.
Client can use the URI to exchange its Mobile Subscription Info
The actual exchange is over HTTPS which is outside of the DHCP, DHCPv6 and RA process
Notes: Shared address cannot be interface addr. ARP
static configuration for address prefix in enterprise case

## Slide 4: Use Case Assumptions
UA roams from MN to WiFi (e.g., home WiFi)
UA uses simple PSK for authentication
In IPv4 environment, DHCPv4 option will be used.
In IPv6 environment, both DHCPv6 and RA options will be used.
The mechanism mimics the Captive-Portal Identification in DHCP and Router Advertisements (RAs) defined in RFC 8910.
Notes: Shared address cannot be interface addr. ARP
static configuration for address prefix in enterprise case

## Slide 5: IPv4-only Client Behavior
Client supports this option should include “Mobile-Sub-Info” in the option in the Parameter Request List in DHCPREQUEST message.
Server may send the “Mobile-Sub-Info” in the DHCP ACK w/o client explicitly requesting.
Client doesn’t support or its policy dictates not to share the info may simply ignore the URI.
Client that supports the exchange may initiates the exchange process over HTTPS with URI.
We propose to use EAP-AKA over HTTPS to exchange the mobile subscription info.
Notes: Shared address cannot be interface addr. ARP
static configuration for address prefix in enterprise case

## Slide 6: DHCP Server Behavior
Server that supports “Mobile-Sub-Info” must includes a URI in the DHCP ACK while receiving a DHCPREQUEST with the option in the Parameter Request List.
Server ”may” include the URI w/o the option in the DHCPREQUEST.
Notes: Shared address cannot be interface addr. ARP
static configuration for address prefix in enterprise case

## Slide 7: IPv6 Client Behavior
Client supports this option should include “Mobile-Sub-Info” in the option in DHCPv6 SOLICIT message.
Upon receiving the URI in REPLY, Client that supports the option may initiates the exchange process over HTTPS with the URI.
We propose to use EAP-AKA over HTTPS to exchange the mobile subscription info.
Notes: Shared address cannot be interface addr. ARP
static configuration for address prefix in enterprise case

## Slide 8: DHCPv6 Server Behavior
Server that supports “Mobile-Sub-Info” must includes a URI in the ADVERTISE and REPLY while receiving ” Mobile-Sub-Info” option in the SOLICIT.
Notes: Shared address cannot be interface addr. ARP
static configuration for address prefix in enterprise case

## Slide 9: RA Behavior
Server supports “Mobile-Sub-Info” must include “Mobile-Sub-Info” in the RA.
Client that supports “Mobile-Sub-Info” may may initiates the exchange process over HTTPS with the URI.
We propose to use EAP-AKA over HTTPS to exchange the mobile subscription info.
Notes: Shared address cannot be interface addr. ARP
static configuration for address prefix in enterprise case

## Slide 10: Some Considerations
Multiple SIM Subscriptions
  Client must use the active data “SIM” subscription for the exchange.
URI Consistency
  Network may support all three methods. It highly recommends to use the same URI to avoid any ambiguity.
Notes: Shared address cannot be interface addr. ARP
static configuration for address prefix in enterprise case